Laser Safety

Self-Audit Checklist

Building ___________     Room ________  Principal Investigator  ____________________

Audit Performed by _____________________________   Date __________

|  | Y | N | NA | COMMENTS |
| --- | --- | --- | --- | --- |
| A. Administrative |
| Lasers are included in inventory: http://www.ehss.vt.edu/programs/laser_safety.php |  |  |  |  |
| 2. Lasers are classified appropriately (3R, 3B, 4) |  |  |  |  |
| 3. Standard operating and alignment procedures are available (attach SOPs) using EHSS template http://www.ehss.vt.edu/detail_pages/document_details.php?document_id=341 |  |  |  |  |
| 4. Viewing cards are used for alignment |  |  |  |  |
| 5. Authorized laser users attended appropriate training (attach record) |  |  |  |  |
| B. Labeling and Posting (attach pictures) |
| 1. Certification label present |  |  |  |  |
| 2. Class designation and appropriate warning label present |  |  |  |  |
| 3. Radiation output information on label |  |  |  |  |
| 4. Aperture label present |  |  |  |  |
| 5. Appropriate warning/danger sign at entrance to laser area |  |  |  |  |
| 6. Warning posted for invisible radiation |  |  |  |  |
| C. Control Measures (attach pictures) |
| 1. Protective housing present and in good condition |  |  |  |  |
| 2. Beam attenuator present |  |  |  |  |
| 3. Laser table below eye level |  |  |  |  |
| 4. Beam is enclosed as much as possible |  |  |  |  |
| 5. Beam not directed toward doors or windows |  |  |  |  |
| 6. Beams are terminated with fire-resistant beam stops |  |  |  |  |
| 7. Surfaces minimize specular reflections |  |  |  |  |
| 8. Controls are located so that the operator is not exposed to beam hazards |  |  |  |  |

| D. Personal Protective Equipment |
| --- |
| 1. Eye protection is appropriate for wavelength and power |  |  |  |  |
| 2. Eye protection is available for authorized users. |  |  |  |  |
| 3. Warning/indicator lights can be seen through protective filters |  |  |  |  |
| E. Class 3b and 4 Lasers |
| 1. Interlocks on protective housing |  |  |  |  |
| 2. Service access panel present |  |  |  |  |
| 3. Limited access to spectators |  |  |  |  |
| 4. Nominal hazard zone determined |  |  |  |  |
| 5. Authorized users do not wear watches or reflective jewelry while laser is operating |  |  |  |  |
| 6. Viewing portals present where MPE is exceeded |  |  |  |  |
| F. Class 4 Lasers |
| 1. Failsafe interlocks at entry to controlled area |  |  |  |  |
| 2. Area restricted to authorized users |  |  |  |  |
| 3. Laser may be fired remotely |  |  |  |  |
| 4. If present, curtains are fire-resistant |  |  |  |  |
| 5. Area designed to allow rapid emergency egress |  |  |  |  |
| 6. Pulsed- interlocks designed to prevent firing of the laser by dumping the stored energy into a dummy load |  |  |  |  |
| 7. CW- interlocks designed to turn off power supply or interrupt the beam by means of shutters |  |  |  |  |
| G. Non-Beam Hazards |
| 1. High voltage equipment appropriately grounded |  |  |  |  |
| 2. High voltage equipment located away from wet surfaces or water sources |  |  |  |  |
| 3. High voltage warning label in place |  |  |  |  |
| 4. Compressed gases secured |  |  |  |  |
| 5. Ventilation used if Laser Generated Air Contaminants |  |  |  |  |

Upon completion of the laser self-audit, please submit this form and attachments to:

Albert Moore, MS, CIH, CPE, CLSO

Laser Safety Officer

EHS (0423)

Or scan paper documents and email the pdf to chronos@vt.edu.

Thank you.